## Slide 1
Chair Balancing Act
A tilt-sensing audio feedback device for fixed-leg chairs
All legs down = silence. Any leg lifts = rising tone. More tilt = louder.
Part safety reminder, part office prank, part gift-shop impulse buy.
Product Overview • Concept Stage • 2026

## Slide 2
Product Overview

## Slide 3
How It Works
Static Balance
SILENCE
All legs on the floor. Device sleeps. No sound at all.
Dynamic Balance
CONTINUOUS RISING TONE
Any leg lifts off the floor. Agreeable low tone begins. Rises smoothly with tilt. Pitch + volume + urgency scale proportionally.
Near Fall
MAXIMUM ALARM
Steep angle, close to tipping point. Tone at peak urgency. Everyone in the room knows what's happening.
The device:
~32 mm round × 10 mm • ~15g • CR2450 coin cell (months of life) • AirTag-sized • Adhesive mount under chair seat • Fixed-leg chairs only

## Slide 4
Architecture & Constraints
SUBSYSTEMS
Accelerometer
Tilt angle on pitch + roll
I2C + wake interrupt
MCU + Firmware
Filter, tone generation, calibration
Reads accel, generates PWM tone
Class-D Amp + Piezo Speaker
Amplifies MCU tone output
PWM input, piezo output
CR2450 Coin Cell
Months of life, user-replaceable
MCU sleeps in static balance
Button
On/off, mode cycle
GPIO
HARD CONSTRAINTS
BOM cost
<$8 at 1k units
Gift/novelty price — retail $15-25
Battery life
>2 months on CR2450
Forget-and-use, no charging
Latency
<100 ms tilt-to-sound
Comedy timing is the product
Size
32 mm × 10 mm, 15g
AirTag-sized, hidden under seat
Data flow: Accelerometer --I2C--> MCU (filter + tone gen) --PWM--> Class-D Amp --> Piezo speaker

## Slide 5
Hardest Problems & Component Tradeoffs
THREE HARDEST PROBLEMS
1
Escalation curve across chair types
School chairs and dining chairs have different fall points and tilt ranges. The continuous tone must start gently at first leg lift and peak just before the fall point — not too early (annoying) or too late (useless). Needs auto-calibration + playtesting.
2
Filtering fidgeting from tilting
Sitting down, crossing legs, leaning to grab something — all produce accelerometer signals. Continuous model means any sustained tilt produces sound — the dead-band and time filter are critical.
3
Designing the continuous tone
The tilt-to-tone mapping IS the product. Must be agreeable at low tilt and urgent near fall. Three modes (serious, comedic, stealth) need distinct character. Needs sound designer + playtesting with kids.
COMPONENT TRADEOFFS
MCU
Cost + PWM
ATtiny ($0.50) has HW PWM for tone gen. STM32L0 ($1.20) has DAC for smoother audio. nRF52 ($3) overkill.
Accelerometer
FW complexity
Cheapest has no filtering — $0.50 more gets on-chip motion detection, saves weeks of FW tuning.
Audio path
Simplicity
MCU PWM + class-D amp ($0.30) replaces audio playback IC. Enables real-time continuous tone, not fixed clips.
Speaker
Physical constraint
Dynamic (4 mm tall, louder) vs. piezo (2.5 mm, fits 10 mm enclosure). Piezo resonance aids escalation.
Power
Simplicity
CR2450 coin cell: no charging circuit, no USB port, months of life, user-replaceable. LiPo only if V2 needs more current.
Hardware is simple. The product lives or dies on the escalation curve — how tilt maps to tone. Playtesting > engineering.

## Slide 6
PRD Summary: 45 Requirements
BY TRACK
Hardware
18 reqs
(8 electrical, 8 mechanical, 4 PCB)
Firmware
18 reqs
(7 core, 4 modes, 4 calibration, 2 power, 1 versioning)
Integration
9 reqs
(end-to-end tests spanning HW + FW)
BY PRIORITY
40 Must-have
5 Should-have
0 Nice-to-have (V2 only)
GATE RESULT
PASS
66 pass / 23 N/A / 1 minor gap (FW versioning scheme)
KEY REQUIREMENTS
FW-C-05
Continuous tone: pitch + volume scale proportionally with tilt
FW-C-06
Real-time tracking: angle change to tone change < 100ms
INT-02
Zero false triggers on transient motion (sitting down, bumping)
FW-PM-04
Battery life >= 6 months at 20 tilt events/day
HW-M-01
Enclosure max 35mm dia x 10mm height
HW-E-06
Total sleep current <= 2 uA (static balance)

## Slide 7
Open Items & V2 Horizon
7 OPEN ITEMS (resolve before production)
M2
Escalation curve tuning across 5+ chair types
M2
Piezo volume validation in real environments
M2
False trigger testing with real users (fidgety kids)
M2
PWM audio quality -- pleasant tone at low tilt?
M2
CPSIA / EN 71 acoustic safety for children's products
M3
Tone design for 3 modes (sound designer + FW)
M3
Adhesive durability testing
V2 (if market validates)
Custom tone profiles via USB
Board respin: USB-C connector, upload escalation curve parameters
BLE + companion app
MCU change: ATtiny -> nRF52. Full board respin + app dev
Adjustable sensitivity
Requires BLE. Depends on V2 BLE decision
Rechargeable battery
Adds charging IC, USB-C, Li-Po. Enclosure redesign
V2 decisions should wait for 6+ months of V1 sales data and customer feedback.